## Slide 1: Mass / Moderator Log Errors
Brandon O’Donnell, NCS Engineer, BWXT Nuclear Operations Group - Lynchburg

## Slide 2: Background
Routine NCS audit of Specialty Fuels Fabrication (SFF) facility in September, 2015 timeframe
Many gloveboxes in SFF facility were authorized to use “tiered” mass / moderator limits
  10 kg 235U / 597 grams moderating material (H/X of 2), OR
  3.6 kg 235U / 2,148 grams moderating material (H/X of 20), OR
  350 grams 235U / no restriction on mass of moderating material
Audit of mass / moderator log entries revealed multiple violations of the moderator mass limit in a specific boxline

## Slide 3: Background
General purpose use glovebox used for operations involving Advanced Gas Reactor (AGR) fuel

## Slide 4: Background
Operations in the SFF facility utilizing mass / moderator limits were immediately suspended
Critique meeting was held with operators, operations management, and NCS
Initially believed that these were simply bookkeeping errors
  Determined during critique meeting that these may not have been bookkeeping errors, but rather actual limit violations
Condition was reported to the Nuclear Regulatory Commission (NRC)

## Slide 5: Background
Discovered during critique meeting that operator understanding was they needed to adhere to the mass limit or the moderation limit, but not both
Extent of condition review revealed similar issues with another glovebox in the SFF facility
Activities in non-SFF areas utilizing mass / moderator limits were temporarily suspended
  Logs reviewed for accuracy – some issues identified, but none rising to the level of additional NRC reporting
  Operators required to demonstrate understanding of NCS limits through training and testing

## Slide 6: Underlying Issues
SFF facility is unique to other areas
  Routinely goes down for extended periods of time (months to years) depending on available work
  Work scopes are constantly changing
  Other plant areas operate with considerably more continuity
The application of mass / moderator limits requires tracking two parameters simultaneously to ensure compliance
  Operator training is paramount
At the time, paper logs were being used
  The “addition / removal” math is a manual process

## Slide 7: Underlying Issues
Paper log

## Slide 8: Corrective Actions
At the time, there was no division-wide policy on suspending and restarting fuel operations, so one was created
  Any operation shutdown for more than 6 months has to be formally removed from service
  Restart of such operations require Change Review Board review and approval
Automated computer based mass / moderator logs implemented in the place of manual paper logs
  Developed by process engineering and goes through layers of safety and QA review
  “Addition / removal” math is done automatically
  Provide visual warnings if an operator attempts to add material that would result in violation of a limit

## Slide 9: Corrective Actions
Areas using mass / moderator logs developed and implemented area specific procedures that provide detailed instructions on the use of mass / moderator logs
  This is used in conjunction with the automated computer based mass / moderator logs
The use of “tiered” mass / moderator limits in the SFF facility was eliminated
  Control scheme developed to meet production needs while being as “operator friendly” as possible
  Operators, process engineers, and management involved every step of the way

## Slide 10: SFF Control Scheme
For a moderation controlled glovebox, what really matters?
  Liquids and other materials that intimately mix with the fuel
Operations desire was to track net weight of material being added to or removed from a glovebox
  Requires no knowledge of the uranium or 235U value
Two modes of operation defined
  “Fuel operations” = large net mass allowed but no liquids, net mass includes both fuel and non-fuel material that will be blended with fuel material
  “Cleanout operations” = insignificant net mass with liquids allowed

## Slide 11: SFF Control Scheme

## Slide 12: SFF Control Scheme
Ingress of liquids is limited in two other ways:
Glovebox integrity
  Passive engineered control
  Maintained through periodic inspections for visible “cracks” in the glovebox structure and seals (such as around windows)
  Transparent to the operator, except when performing maintenance activities which may degrade glovebox integrity
Prohibition on use of water during fire fighting
  Administrative control
  Managed by the Emergency Operations Center (EOC) in the event of a fire

## Slide 13: Key Lessons Learned
Operations need a formalized policy on suspending and restarting fuel operations
Complicated control schemes like the use of “tiered” mass / moderator limits need robust operator aides, and training is paramount
All facilities should employ NCS control schemes that leave little room for interpretation
  Especially true for facilities that routinely go down for extended periods of time or with constantly changing work scopes

## Slide 14: Audience Discussion
How are facilities like the SFF handled elsewhere?
How are others handling control schemes like the “tiered” mass / moderator limits?
How are suspending and restarting fuel operations handled elsewhere?