## Slide 1: Study of Whisper Statistics for Criticality Safety Code Validation
Natasha Glazener, Trevor Stewart, Alan Yamanaka
6-14-17
LA-UR-17-24374

## Slide 2: How many particles?
Whisper : the Sensitivity/Uncertainty software package developed for MCNP
MCNP – typical use | 
100 active cycles | 10,000 n/cycle
MCNP – for Whisper | 
500 active cycles | 100,000 n/cycle
How many particles does Whisper really need?

## Slide 3: Variable Space
Tracked Variables | Test Variables | Constants
Benchmark Selection USL Run Time Benchmark Weight / correlation | Neutron Histories Materials Geometry | Cycles .80c libraries S(α,β) Temperature
10,000 n/cycle
25,000 n/cycle
50,000 n/cycle
100,000 n/cycle

## Slide 4: Representative Models
More uncommon materials
More unusual geometry
239 Pu Spheres
Fuel Assemblies
HS-Pu
Tantalum Reflectors
Compound Reflectors
239 Pu glovebox
HS-Pu glovebox
Exotic fuel kernels

## Slide 5: Correlation Coefficient
Depending on which theory document referenced, ck should be 0.8 or 0.9 to have very high confidence in the correlation & results.
Correlation between 2 models due to nuclear data

## Slide 6: Basic Decks
 |  | N/Cycle | USL | # BM's | High ck
Jezebel | PU-MET-FAST-001 | 100 | 0.98078 | 42 | 1.0000
 |  | 50 | 0.98075 | 44 | 0.9998
 |  | 25 | 0.98062 | 44 | 0.9994
 |  | 10 | 0.98053 | 46 | 0.9995
PURNIMA-I | PU-COMP-FAST-004 | 100 | 0.97387 | 69 | 0.9883
 |  | 50 | 0.97387 | 69 | 0.9888
 |  | 25 | 0.97371 | 69 | 0.9885
 |  | 10 | 0.97381 | 69 | 0.9883
HEU Cylinder | HEU-MET-FAST-050 | 100 | 0.97560 | 172 | 0.9998
 |  | 50 | 0.97538 | 181 | 0.9993
 |  | 25 | 0.97521 | 178 | 0.9988
 |  | 10 | 0.97442 | 178 | 0.9982

## Slide 7: More Complicated Decks
 | N/Cycle | USL | # BM's | High ck
239Pu flooded ingot mold | 100 | 0.97900 | 64 | 0.9538
 | 50 | 0.97905 | 64 | 0.9544
 | 25 | 0.97883 | 64 | 0.9532
 | 10 | 0.97865 | 64 | 0.9514
HS-Pu solution spheres | 100 | 0.96443 | 96 | 0.9291
 | 50 | 0.96438 | 98 | 0.9300
 | 25 | 0.96423 | 93 | 0.9279
 | 10 | 0.96455 | 95 | 0.9298
Stacked 239Pu shells with thick water | 100 | 0.97856 | 68 | 0.9308
 | 50 | 0.97846 | 68 | 0.9304
 | 25 | 0.97813 | 70 | 0.9251
 | 10 | 0.97849 | 69 | 0.9285

## Slide 8: We didn’t forget U
 |  | N/Cycle | USL | # BM's | High ck
HEU Slabs with Hydrogen-based Moderators | HEU-MET-FAST-007 | 100 | 0.98226 | 68 | 0.9857
 |  | 50 | 0.98220 | 68 | 0.9849
 |  | 25 | 0.98205 | 68 | 0.9836
 |  | 10 | 0.98227 | 68 | 0.9849
Fictional U “reactor” with Ru reflector |  | 100 | 0.97449 | 106 | 0.8621
 |  | 50 | 0.97430 | 108 | 0.8572
 |  | 25 | 0.97400 | 109 | 0.8531
 |  | 10 | 0.97315 | 113 | 0.8328
Above with Xe added |  | 100 | 0.89985 | 79 | 0.1458
 |  | 50 | 0.90010 | 74 | 0.1415
 |  | 25 | 0.90033 | 75 | 0.1398
 |  | 10 | 0.90001 | 79 | 0.1357

## Slide 9: When Whisper isn’t the right tool
 | N/Cycle | USL | # BM's | High ck
Pu-Be sphere | 100 | 0.95250 | 190 | 0.7752
 | 50 | 0.95260 | 190 | 0.7758
 | 25 | 0.95260 | 190 | 0.7783
 | 10 | 0.95254 | 190 | 0.7821
233U flooded ingot mold | 100 | 0.94339 | 126 | 0.7679
 | 50 | 0.94340 | 126 | 0.7673
 | 25 | 0.94330 | 126 | 0.7694
 | 10 | 0.94348 | 126 | 0.7712
232Th flooded ingot mold | 100 | 0.93521 | 142 | 0.0092
 | 50 | 0.93524 | 137 | 0.0092
 | 25 | 0.93525 | 136 | 0.0092
 | 10 | 0.93549 | 141 | 0.0093

## Slide 10: Benchmark Ordering
pu-met-fast-027-001.i | pu-met-fast-027-001.i | pu-met-fast-027-001.i
pu-met-fast-011-001.i | pu-met-fast-011-001.i | pu-met-fast-011-001.i
pu-met-fast-044-004.i | pu-met-fast-044-004.i | pu-met-fast-044-004.i
pu-met-fast-031-001.i | pu-met-fast-031-001.i | pu-met-fast-031-001.i
pu-met-fast-044-005.i | pu-met-fast-044-005.i | pu-met-fast-044-005.i
pu-met-fast-044-003.i | pu-met-fast-044-003.i | pu-met-fast-044-003.i
pu-met-fast-036-001.i | pu-met-fast-036-001.i | pu-met-fast-036-001.i
pu-met-fast-044-002.i | pu-met-fast-044-002.i | pu-met-fast-044-002.i
pu-met-fast-024-001.i | pu-met-fast-024-001.i | pu-met-fast-024-001.i
pu-met-fast-021-002.i | pu-met-fast-021-002.i | pu-met-fast-021-002.i
pu-met-fast-044-001.i | pu-met-fast-044-001.i | pu-met-fast-044-001.i
pu-met-fast-016-002.i | pu-met-fast-016-002.i | pu-met-fast-016-002.i
pu-met-fast-016-006.i | pu-met-fast-016-006.i | pu-met-fast-016-006.i
pu-met-fast-016-003.i | pu-met-fast-023-001.i | pu-met-fast-016-003.i
pu-met-fast-023-001.i | pu-met-fast-016-003.i | pu-met-fast-023-001.i
pu-met-fast-016-005.i | pu-met-fast-016-005.i | pu-met-fast-016-005.i
pu-met-fast-016-004.i | pu-met-fast-016-004.i | pu-met-fast-016-004.i
pu-met-fast-018-001.i | pu-met-fast-018-001.i | pu-met-fast-018-001.i
pu-met-fast-021-001.i | pu-met-fast-021-001.i | pu-met-fast-021-001.i
pu-met-fast-038-001.i | pu-met-fast-038-001.i | pu-met-fast-038-001.i
pu-met-fast-045-005.i | pu-met-fast-045-005.i | pu-met-fast-045-005.i
pu-met-fast-009-001.i | pu-met-fast-009-001.i | pu-met-fast-009-001.i
pu-met-fast-019-001.i | pu-met-fast-019-001.i | pu-met-fast-019-001.i
pu-met-fast-030-001.i | pu-met-fast-030-001.i | pu-met-fast-030-001.i
pu-met-fast-035-001.i | pu-met-fast-035-001.i | pu-met-fast-035-001.i
pu-met-fast-022-001.i | pu-met-fast-022-001.i | pu-met-fast-022-001.i
mix-met-fast-007-022.i | mix-met-fast-007-022.i | mix-met-fast-007-022.i
mix-met-fast-009-001.i | mix-met-fast-009-001.i | pu-met-fast-014-001.i
pu-met-fast-014-001.i | pu-met-fast-014-001.i | mix-met-fast-009-001.i
pu-met-fast-025-001.i | pu-met-fast-025-001.i | pu-met-fast-025-001.i
mix-met-fast-007-014.i | mix-met-fast-007-014.i | mix-met-fast-007-014.i
pu-met-fast-001-001.i | pu-met-fast-001-001.i | pu-met-fast-045-001.i
pu-met-fast-045-001.i | pu-met-fast-045-001.i | pu-met-fast-001-001.i
mix-met-fast-007-023.i | mix-met-fast-007-023.i | mix-met-fast-007-023.i
pu-met-fast-045-002.i | pu-met-fast-045-002.i | pu-met-fast-045-002.i
pu-met-fast-045-003.i | pu-met-fast-045-004.i | pu-met-fast-045-004.i
pu-met-fast-045-004.i | pu-met-fast-045-003.i | pu-met-fast-045-003.i
mix-met-fast-007-015.i | mix-met-fast-007-015.i | mix-met-fast-007-015.i
mix-met-fast-007-019.i | mix-met-fast-007-019.i | mix-met-fast-007-019.i
pu-met-fast-040-001.i | pu-met-fast-040-001.i | pu-met-fast-040-001.i
pu-met-fast-029-001.i | pu-met-fast-029-001.i | pu-met-fast-029-001.i
mix-met-fast-001-001.i | mix-met-fast-001-001.i | mix-met-fast-007-007.i
mix-met-fast-007-020.i | mix-met-fast-007-007.i | mix-met-fast-001-001.i
mix-met-fast-007-007.i | mix-met-fast-007-020.i | mix-met-fast-007-020.i
pu-met-fast-008-001.i | pu-met-fast-008-001.i | pu-met-fast-008-001.i
mix-met-fast-005-001.i | pu-met-fast-045-007.i | pu-met-fast-045-007.i
pu-met-fast-045-007.i | mix-met-fast-005-001.i | mix-met-fast-005-001.i
pu-met-fast-026-001.i | pu-met-fast-026-001.i | pu-met-fast-026-001.i
pu-met-fast-045-006.i | pu-met-fast-045-006.i | pu-met-fast-045-006.i
pu-met-fast-032-001.i | pu-met-fast-032-001.i | pu-met-fast-032-001.i
pu-met-fast-003-103.i | pu-met-fast-015-001.i | pu-met-fast-015-001.i
pu-met-fast-015-001.i | pu-met-fast-003-103.i | pu-met-fast-003-103.i
mix-met-fast-003-001.i | mix-met-fast-003-001.i | mix-met-fast-003-001.i
mix-met-fast-007-008.i | mix-met-fast-007-008.i | mix-met-fast-007-008.i
mix-met-fast-007-016.i | mix-met-fast-007-016.i | mix-met-fast-007-016.i
mix-met-fast-007-021.i | mix-met-fast-007-021.i | mix-met-fast-007-021.i
pu-met-fast-028-001.i | pu-met-fast-028-001.i | pu-met-fast-028-001.i
mix-met-fast-007-017.i | mix-met-fast-007-017.i | mix-met-fast-007-017.i
mix-met-fast-007-009.i | mix-met-fast-007-009.i | mix-met-fast-007-009.i
pu-met-fast-002-001.i | pu-met-fast-002-001.i | pu-met-fast-002-001.i
pu-met-fast-012-001.i | pu-met-fast-012-001.i | pu-met-fast-012-001.i
mix-met-fast-007-018.i | pu-comp-fast-004-001.i | pu-comp-fast-004-001.i
mix-met-fast-010-001.i | mix-met-fast-007-018.i | mix-met-fast-007-018.i
pu-comp-fast-004-001.i | mix-met-fast-010-001.i | mix-met-fast-010-001.i

## Slide 11: Take Aways
Minor variations in the weighting/ordering of Benchmarks
Standard Deviations of USL ~10-4 or 10-5
Did not see false positives at lower n/cycle
A little light on U cases
Didn’t test temp or other advanced features
Positive trend in ck for low ck
  Trends were small (<0.01)